## Slide 1: The Future of Human and Space Research: The Lagrange Communication Advanced Realtime Space-weather (LCARS) Array A NASA Mission Concept
Presented by
Dr. Jerry W. Manweiler – Fundamental Technologies, LLC, Lawrence, KS (KU:PhD-’97,MS-’87,BS-’85)
For the University of Kansas Department of Physics and Astronomy SpaceFest - 2025
In honor of the retirement of Prof. Thomas E. Cravens and Prof. Hume Feldman
© 2025 – Fundamental Technologies, LLC; All Rights Reserved; Do Not Duplicate without Prior Written Permission - 1 -

## Slide 2: LCARS Array website and Publications https://LCARS.FTecs.com
© 2025 – Fundamental Technologies, LLC; All Rights Reserved; Do Not Duplicate without Prior Written Permission - 2 -
Decadal White Paper AGU 2022 Poster AGU 2023 Poster
AGU 2024 Poster LCARS Website

## Slide 3
In 2020 Dr. Nicola Fox held the NASA’s Heliophysics 2050 Workshop’s and asked the question:
What should Humanities Space Exploration and Expansion into the Solar System look like by the year 2050?
LCARS Array Vision Driving Question
© 2025 – Fundamental Technologies, LLC; All Rights Reserved; Do Not Duplicate without Prior Written Permission - 3 -
Assumptions:   By the year 2050 there will be  
  A Lunar Base with extensive communications capabilities
  Humans on Mars – and since they won’t be coming back, we call that a Base!
  Significant expansion of NASAs Heliophysics System Observatory by sending multiple different spacecraft to the outer planets, to Mars, to the Asteroid belts, etc.
  Interstellar Probe will be on its way and New Horizons will still be working
    (Note: Voyager unfortunately will be dead in the VLISM)

## Slide 4
Space weather and Solar Science
  Understanding of The radiation environment in space otherwise called, Space weather, is critical to human exploration
  The number of historical and current missions in support of space weather research has allowed us a fundamental understanding of the overall impact that the Sun has on Earth's systems
    The ACE, SOHO, WIND, STEREO A/B ,Solar Probe and Solar Orbiter missions providing discoveries beyond their original mission goals, but they can’t see the “whole” sun all the time
  Space weather modeling accuracy demands a “whole” sun view allowing incremental and sometimes significant improvement in the ability to accurately predict times when Earth space assets are at risk as well as future Human assets in the solar system (Mars etc.)
  There is critical need for highly accurate space weather predictions for human presence on the Moon and Mars since both bodies spend significant amount of time in the Solar Wind exposed to Space Weather without a magnetic shield
So…
Why the LCARS Array – Now?
What are the problems of the present and near future that need to be addressed?
Data and Communications
  Manned Exploration of the solar system requires a large volume of data to be constantly streamed from all of the missions back to earth
  The Data volume by current (and to be flown) NASA missions has exploded exponentially heading into the 10’s of TB / day
  Instrument capabilities are limited by bandwidth even with modern compression algorithms (lossless or lossy)
  High bandwidth Communications is very limited through Earth’s atmosphere
  With some success, the recently tested Laser communications is also has issues due to need to maintain pointing
© 2025 – Fundamental Technologies, LLC; All Rights Reserved; Do Not Duplicate without Prior Written Permission - 4 -

## Slide 5
The LCARS Array – the Lagrange Points
© 2025 – Fundamental Technologies, LLC; All Rights Reserved; Do Not Duplicate without Prior Written Permission - 5 -
Lagrange Points for the Earth-Sun System showing the orbits of Mercury, Venus, Earth, and Mars

## Slide 6
LCARS Vision
© 2025 – Fundamental Technologies, LLC; All Rights Reserved; Do Not Duplicate without Prior Written Permission - 6 -
Space Platform (station) at each of the Earth-Sun Lagrange Points
Idealized Lunar Communications
L2 is protected and offers redundant comms
L4 has unobstructed view of L3 and sits upstream of Space Weather flow along the Parker spiral
L3 is behind the sun and can see L4 and L5, offers communications for missions obscured by sun
Each station includes Advanced modular multi-bay Solar and in-situ instruments with Ejectable and dock able sensors Observation Platform shields comms unit
Advanced Station Comms: Multi-frequency Multi-channel
Terahertz/Laser Network Comms
Advanced Gimbled Deep Space Dish
L5 has unobstructed view of L3 and sits downstream of Space Weather flow along the Parker spiral
L1 is an upstream Space Weather Detector
Earth-Lunar Comms
The SOL-Network is an Interstation communications Network using Terahertz/Laser comms with AI based packet networking

## Slide 7
The LCARS Array – the Spacecraft Concept
  The LCARS Array Spacecraft Concept
  Novel Spacecraft Development
  100 Year Mission Lifetime Goal
    Multi-Component Modular Spacecraft
    One or more transport rockets to units'
    Station Keeping engine at final destination
    Modular Spacecraft Design with Self Assembly capability
  Separate Communications and Sensor Sections
  Communications Section
    Inter-SC COMM (Laser +Terahertz)
    Multichannel/Multifrequency Radio Comms
    Gimbled Deep Space Communications
  Sensor Section
    Current Sizing: 4 m tall x 2-3 m deep
    Sensor Section SHIELDS the Communications Array!
    Modular Instrument Bays, 4 m tall x 28 m
      1 m2 sections divided as 1 dm2 units
      Power and Data per unit
      Up to 100 units per section and 2800 total units
    Direct Solar Telescopes with continuous recording
    In-Situ Solar Wind Instruments with continuous recording scattered throughout the available bays
    Stellar telescopes instruments on available side and rear looking bays
© 2025 – Fundamental Technologies, LLC; All Rights Reserved; Do Not Duplicate without Prior Written Permission - 7 -
4 meters tall
2-3 meters deep
Data and Command and Control Systems

## Slide 8
The LCARS Array – the Instrument Deck
  The LCARS Array Spacecraft Concept
  Instrument Section
    Modular Instrument Bays
    Direct Solar Telescopes with continuous recording
      Photospheric Imager
      Solar Magnetograms
      Coronal Imager
      Coronal Spectrogram
      etc.
    In-Situ Solar Wind Instruments with continuous recording
      Cosmic Ray Particle Detectors
      Plasma Sensors, e.g.
        Top-Hat Detectors
        Langmuir Probes
      Magnetic Field Antennae and Internal Sensors
      Electric Field Antennae and Spacecraft Charging Sensors
    Rear facing internal outward facing elements provide space for background measurements to calibrate other instruments
© 2025 – Fundamental Technologies, LLC; All Rights Reserved; Do Not Duplicate without Prior Written Permission - 8 -

## Slide 9
The LCARS Array – Technology
  The LCARS Technology Development
  Novel Communication Technologies
    Inter-SC COMM (Laser +Terahertz Gimbled)
    Autonomous Networking
  Hardware:
    Terahertz and Laser Communications Systems
    Gimbled Deep Space Communications Dish
    Multichannel/Multifrequency Radio Comms
  Protocols:
    Interplanetary Communication Protocols (up to 18 minute packet delays)
    Adaptive and Predictive AI protocol evolution
  Adaptive Deep Space Dish Capabilities:
    Gimbled pointing
    Central receiver
    Lightweight Dish materials (e.g. Mylar)
    Deployable and Retractable Dish
    Variable Dish Surface Area w/ R <= 35m
  Novel Spacecraft Technologies
    Multi-Component Modular Spacecraft
    One or more transport rockets to final destination
    Station Keeping engine at final destination
    Modular Spacecraft Design with Self Assembly capability
  Novel Software Systems
    Self-writing (AI) Adaptive Software Systems
    Self-healing (AI) Redundant Software Systems
    Adaptive / Predictive Data Analytics – e.g. Predictive Decision Making onboard each Space station
© 2025 – Fundamental Technologies, LLC; All Rights Reserved; Do Not Duplicate without Prior Written Permission - 9 -
  The LCARS Technology Development
  Novel Sensor Module Technologies
    Modular Instrument Bays
    Self-Docking Modules
    Spacecraft ejection of defective modules
  Data System Technologies
    Large Redundant Data System
    Photonic or Quantum Storage Technologies
    Large Redundant Data Systems
    Self-Healing Hardened Systems
    Storage Module Ejection and Replacement
    Autonomic Data Management
  Novel Power System Capability
    Solar Panels used for minimum power requirements
    Replaceable Solar Arrays and Fuel Cells
    Embedded Fuel Cell Array used for Operations
      Primary power for Comms
  Power provided per Bay Unit for experiments
    Each bay unit provides Vmax power
    Coupled bays provide N*Vmax power

## Slide 10
LCARS Array – Into the Future
  Additional LCARS Array can be deployed at other Lagrange points.
  The Earth Moon Lagrange points (trial)
  The Mars Sun Lagrange points
    Different orbital cadence
    Provides the capability to significantly enhance the overall SOL-Network
    The orbital period of this LCARS Array would be different providing additional continuous coverage of deep space assets
  What about the Mercury Sun Lagrange Points
    This would give an LCARS Array Solar Observatory at 0.3 AU (near the current Solar Orbiter distance)
    The enhancement to direct and immediate measurement of the in-situ Space Weather would greatly increase the predictive powers of the Space Weather Modeling systems
  What about Jupiter, Saturn, Uranus, or Neptune?
LCARS Array – The Future
© 2025 – Fundamental Technologies, LLC; All Rights Reserved; Do Not Duplicate without Prior Written Permission - 10 -